## Slide 1: Implementation of Frequency Division Multiplexing using BASK Modulation and Demodulation in MATLAB: From Surname-to-Binary Conversion to Recovery and Verification

## Slide 2: Objective
Simulate digital communication process for transmitting two surnames: DAS and BISWAS.
Convert each surname into binary vector (MSB-first).
Represent signals in time domain using unipolar NRZ.
Apply BASK modulation with different carriers (x1: 2 Hz, x2: 4 Hz).
Combine using FDM and add Gaussian noise.
Demultiplex, demodulate, and decode to verify recovered surnames.

## Slide 3: Theory
NRZ Signaling: Represents digital bits as voltage levels (1 → high, 0 → low).
BASK Modulation: Binary Amplitude Shift Keying – amplitude of carrier represents bit.
Frequency Division Multiplexing (FDM): Combine multiple signals with different carrier frequencies.
Demodulation: Recover original bits by multiplying with carrier and low-pass filtering.
ASCII Conversion: Binary → Characters to verify recovered surnames.
Include small diagram showing bit → NRZ → BASK → FDM → Demodulation → recovered bit → ASCII

## Slide 4: Task 1 – Generate Binary Vectors
Points:
Input surnames: x1 = DAS, x2 = BISWAS.
Converted to binary vectors using ASCII table (MSB-first).
Example:
  DAS → 01000100 01000001 01010011
  BISWAS → 01000010 01001001 01010011 01010111 01000001 01010011

## Slide 5
Input: Surnames 'DAS' and 'BISWAS’.
Function: asc2bn converts text → ASCII → 8-bit binary
Output: Displays binary streams for both surnames

## Slide 6: Task 2 – Represent in Time Domain (NRZ)

## Slide 7: Task 3 – Apply BASK Modulation
x1 modulated with 2 Hz carrier, x2 with 4 Hz carrier.
High bit → carrier present (amplitude 5V), Low bit → no carrier. Successfully transmitted two surnames via BASK + FDM.
MSB-first encoding and decoding ensured correct recovery.
Noise (SNR = 15 dB) did not affect final output.
Demonstrates fundamental concepts of digital communication.

## Slide 8: Task 4 – Frequency Division Multiplexing (FDM)
Input: Binary streams of 'DAS' and
'BISWAS'.
BASK Modulation:
Carrier frequencies: 2 kHz (DAS), 4 kHz (BISWAS)
Amplitude: 1 V for 1, 0 V for 0
FDM Composite: Signals are zero-padded, summed to form a composite signal.
Noise Addition: AWGN with 15 dB SNR added to the composite signal.
Output: Plot of noisy composite BASK signal

## Slide 9: Task 5 – Demultiplexing and Demodulation
Multiply noisy signal with carrier
Detect bit energy and compare with threshold.
Rebuild NRZ signal from recovered bits.
Plot recovered NRZ for DAS (blue) and BISWAS (red).

## Slide 10: Task 6 – ASCII Decoding and Verification
Convert surnames to binary (8-bit per character).
Reshape binary into 8-bit groups.
Convert binary back to decimal → ASCII characters.
Display original and recovered surnames.
Check if recovery is correct.
Output
Original Surnames: DAS BISWAS Recovered Surnames: DAS BISWAS Success: Surnames recovered correctly!

## Slide 11: Results Analysis
NRZ signals correctly represented digital bits.
BASK modulation successful with proper carrier frequencies.
FDM combined signals effectively; noise caused small fluctuations but did not affect recovery.
Demodulation recovered exact binary sequences.
ASCII decoding verified successful transmission of DAS and BISWAS.

## Slide 12
Successfully transmitted two surnames via BASK + FDM.
MSB-first encoding and decoding ensured correct recovery.
Noise (SNR = 15 dB) did not affect final output.
Demonstrates fundamental concepts of digital communication.

## Slide 13: Advantages & Limitations
Advantages
Simple and clear demonstration of digital communication workflow.
Works with noisy channels (robust to moderate noise).
Illustrates NRZ, BASK, FDM, and ASCII encoding/decoding.
Limitations
Low carrier frequencies (2 Hz & 4 Hz) → not practical for real applications.
High sampling rate required for accurate NRZ/BASK plots.
Only two signals simulated; adding more increases complexity.